## Slide 1
Anomaly Dataset — Labels and Features
5,621 labelled samples · 19 features per sample · 4 anomaly classes
Labels (4 classes)
0 — Normal
Network running cleanly. No stress, no impairment. 2,063 samples
1 — Scheduler Fault
gNB real-time thread priority lowered by the OS — misses 1ms slot deadlines. 462 samples
2 — Traffic Flood
UE blasted with UDP traffic exceeding uplink capacity. Simulates a DDoS overload. 936 samples
3 — Channel Degradation
RF impairments injected via the channel broker: fading, noise, burst drops. 2,160 samples
Features (19 per sample)
Hook Latency (p99) — 8 features
* fapi_ul_tti_request p99 ← key fault detector
· fapi_dl_tti_request p99
· pdcp_ul_deliver_sdu p99
· pdcp_ul_rx_data_pdu p99
· rlc_ul_rx_pdu p99
· rlc_ul_sdu_delivered p99
· rlc_dl_tx_pdu p99
· fapi_ul_tti_request max
MAC / Radio — 8 features
· harq_mcs_avg — average modulation order
· harq_mcs_min — worst-slot modulation
· harq_cons_retx — consecutive retransmissions
· harq_fail_rate — HARQ failure rate
· crc_sinr_avg — average signal quality
· crc_harq_fail — CRC-level HARQ failures
· crc_success_rate — transmission success rate
· bsr_kb — UE uplink buffer size
RLC Layer — 3 features
· rlc_throughput_kb · rlc_lat_avg_us · rlc_lat_max_us
Key insight: hook_p99_us_fapi_ul is the only feature that detects scheduler faults — invisible to all standard metrics