## Slide 1
jBPF vs Standard Metrics — What Were We Trying to Prove?
Week 7 evaluation — running both telemetry channels simultaneously on the same gNB
The Setup
We ran both telemetry systems on the same gNB at the same time: jBPF codelets → InfluxDB 1.x | Standard metrics → InfluxDB 3 57 minutes of steady-state traffic with Rician fading channel
Three Questions
1. Do both systems agree where they measure the same thing? 2. Why do the numbers differ even for the same metric? 3. What can jBPF see that standard metrics simply cannot?
Finding 1 — They Agree
Where both measure the same signal (SINR, MCS, CQI, BLER), values match within 1.5%. The codelets are extracting correct data.
Finding 2 — Differences Are Expected
Throughput shows a 1.95× gap because jBPF measures at the application layer while standard metrics measure at the MAC layer — two valid measurements of different things.
Finding 3 — jBPF Sees What Standard Cannot
Hook latency, per-slot FAPI data, RLC/PDCP counters, RRC/NGAP procedure timing — none of these exist in the standard interface. Infrastructure faults are invisible without them.
Conclusion: jBPF is not a replacement for standard metrics — it is a complementary layer that adds depth, resolution, and fault visibility that standard monitoring cannot provide.

## Slide 2
jBPF vs Standard Metrics — Capability Comparison
What each telemetry channel can and cannot measure
Capability
Standard Metrics
jBPF (Janus)
Update rate
~1 s aggregates
Configurable — down to 1 ms per slot
Per-slot (1 ms) visibility
No
Yes
SINR / MCS / CQI / BLER
Yes
Yes
Hook execution latency
No
Yes — 22 hooks (p50/p99/max)
Infrastructure fault detection
No
Yes — only via hook latency
Per-layer byte counters
No
Yes — RLC and PDCP separately
RLC SDU delivery latency
No
Yes
RRC / NGAP procedure timing
No
Yes — per-event timestamps
Scheduling latency histograms
Yes
No
PHR / Rank Indicator
Yes
No
Metric count
~30 fields, 1 table
60+ fields, 17 measurements
CPU overhead
Negligible
~3.3% of one CPU core