## Slide 1
Real-Time Telemetry in Open AI RAN
using Microsoft Janus (jBPF)
Midterm Progress Report
Maxim Bitiu · Bachelor Thesis · April 2026
srsRAN Project · jBPF / Microsoft Janus · ZMQ Virtual Radio · InfluxDB · Grafana

## Slide 2
Why Build This?
The problem with standard 5G network monitoring
Standard 5G monitoring gives you ~1-second averages at the MAC layer only:
• "MCS dropped from 27 to 22" — but why? Radio problem? Scheduler overloaded? Traffic flood?
• No way to tell from standard metrics alone
eBPF (extended Berkeley Packet Filter) lets us inject probes into any running program:
• Zero kernel changes — probes load and unload at runtime
• Per-event granularity at every 1 ms radio slot
• Multiple protocol layers simultaneously
Microsoft Janus (jBPF) extends eBPF to userspace gNB software:
• Hook directly into the srsRAN gNB source code at 22 function call sites
• Capture microsecond-level events invisible to any standard interface
Research Question
Can jBPF hook telemetry distinguish infrastructure faults from channel impairments in a live 5G NR system?
Answer: Yes — and the standard metrics channel cannot do this at all.

## Slide 3
What We Built
A complete 5G NR telemetry pipeline — no physical radio hardware required

## Slide 4
Getting It to Run — Baremetal Installation Challenges
Several non-trivial fixes were needed before any telemetry could flow
Challenge 1: eBPF Verifier Failures
• All 10 MAC codelets had eBPF verifier errors and refused to load
• Hash map relocation types didn't match runtime expectations
• JBPF_HASHMAP_CLEAR loops rejected (too complex for verifier)
• Fix: corrected map definitions + removed clear loops → stats now cumulative
Challenge 2: jrtc-ctl Bug — HARQ Schema Collision
• DL and UL HARQ share the same .proto schema name
• jrtc-ctl's map[string][]byte overwrote DL with UL at registration
• Fix: changed to map[string][][]byte + append() in Go source
Challenge 3: Context Cancellation Race
• errgroup context cancelled phase-2 codelet load when phase-1 (decoder) finished
• Fix: split into two sequential errgroups with independent contexts
Challenge 4: gNB Config YAML Keys
• enable_json_metrics and enable_metrics_subscription do NOT exist
• Correct key is metrics: enable_json: true
• Wrong keys cause silent gNB startup failure (IPC socket never appears)
Challenge 5: IPC Socket Timing
• jrtc must start before gNB — IPC socket /tmp/jbpf/jbpf_lcm_ipc
• created by gNB only after connecting to jrtc shared memory
• Kill-9 leaves stale socket → launch script waits forever
• Fix: clean shutdown script + 20s timeout with permission fix
Result: after all fixes — zero missing-schema errors, all 17 streams flowing

## Slide 5
What We Hooked — 22 Instrumentation Points, 17 Schemas
Coverage across every layer of the 5G gNB software stack
MAC Scheduler
FAPI (PHY↔MAC)
RLC / PDCP
Control Plane RRC / NGAP
Performance Meta
harq_stats (MCS, retx, HARQ state)
crc_stats (SINR, CRC success rate)
bsr_stats (UE buffer occupancy)
uci_stats (CQI, SR, Timing advance)
fapi_dl_config (DL MCS, PRB, TBS per slot)
fapi_ul_config (UL scheduler decisions)
fapi_crc_stats (PHY CRC, SNR hist)
rlc_ul/dl_stats (SDU latency, retx bytes)
pdcp_ul/dl_stats (per-bearer byte counters)
rach_stats (per-RACH SNR + timing adv.)
rrc_procedure (setup, reconfig, reestablishment)
ngap_procedure (core network round-trip)
jbpf_out_ perf_list p50/p90/ p95/p99 per hook ★ Novel metric no standard equivalent
★ jbpf_out_perf_list is the ONLY signal sensitive to infrastructure faults — completely invisible to any standard 5G monitoring interface

## Slide 6
45-Panel Real-Time Dashboard
Live Grafana dashboard — every metric from every layer in one view
Dashboard sections:
• MAC layer (8 panels) — HARQ, SINR, MCS, CRC, BSR, CQI
• RLC / PDCP (10 panels) — SDU latency, throughput bytes, queue depth
• FAPI (6 panels) — per-slot scheduler decisions, PRB utilisation
• jBPF hook latency (8 panels) — p50/p90/p95/p99 per hook
• RRC / NGAP events (5 panels) — attach/detach, procedure timing
• UE application layer (5 panels) — iperf3 UL/DL Mbps, ping RTT, jitter, loss
• Summary + histograms (9 panels) — at-a-glance health
Auto-refresh: 5 s · InfluxDB 1.x backend · InfluxQL queries

## Slide 7
ZMQ Channel Broker — Simulating Real RF Conditions
GRC Python broker intercepts IQ samples between gNB and UE
Two broker implementations:
• C broker: AWGN + Rician/Rayleigh flat fading (fast, stable)
• GRC Python: + EPA/EVA/ETU 3GPP profiles, CFO, burst drops, live GUI
Recommended config:
• K=3 dB Rician, SNR=28 dB, fd=5 Hz
• Pure Rayleigh crashes UE in ~2 min
Processing budget:
• DL: 413 µs · UL: 503 µs
• < 1 ms slot budget with 500 µs headroom

## Slide 8
Janus vs Standard Metrics — What Each Channel Sees
Live side-by-side comparison run during Week 7 evaluation

## Slide 9
The 1.95× Throughput Difference — Not a Bug
Both systems are correct — they measure at different protocol layers
iperf3 sends 10 Mbps of UDP payload.
The standard srsRAN dashboard reads the MAC-layer bitrate: 19.45 Mbps.
The extra 9.45 Mbps comes from:
• Protocol headers: IP (20B) + UDP (8B) + GTP-U (16B) + PDCP (3B) + RLC (2B)
• MAC control elements: BSR, PHR, timing advance
• HARQ overhead: scheduled bytes count even for retransmissions
• PDCCH/reference signals: resource grant signalling
Radio metrics (SINR, MCS, CQI, BLER) agree with r > 0.88.
The mismatch is in throughput only — expected, not an error.

## Slide 10
CPU Overhead — Measured from the Telemetry Itself
jbpf_out_perf_list records hook execution time — no external profiler needed

## Slide 11
Anomaly Datasets — 35 Scenarios, 5 621 Labelled Samples
Week 9 deliverable: AI-ready CSV + HDF5 with microsecond timestamps
4 anomaly classes:
• normal (0) — 2 063 samples — clean baseline
• scheduler_fault (1) — 462 samples — RT thread demotion
• traffic_flood (2) — 936 samples — UDP/TCP flood
• channel_degradation (3) — 2 160 samples — RF impairments
19 features per 1-second window:
• 7 × hook_p99_us (per steady-state hook)
• HARQ: mcs_avg, mcs_min, cons_retx, fail_rate
• CRC: sinr_avg, harq_fail, success_rate
• BSR: bsr_kb
• RLC: throughput_kb, lat_avg_us, lat_max_us
Scenario-based train/test split · train: 4 487 rows · test: 1 134 rows · Feature scaler saved
Key finding: 14 of 23 stress scenarios produce signatures invisible to standard metrics.
hook_p99_us_fapi_ul spikes to >7 000 µs (7× the 1 ms slot budget) during scheduler demotion while SINR/MCS remain normal — impossible to detect without hook latency.

## Slide 12
The Core Result — Hook Latency Identifies Infrastructure Faults
A metric that exists nowhere in standard 5G monitoring
What happened:
• gNB threads demoted from SCHED_FIFO:96 to SCHED_BATCH
• OS scheduler deprioritises them — slot processing delayed
• hook_p99_us_fapi_ul: 6 µs → 7 289 µs (1200× spike)
What standard metrics show:
• Slight MCS drop (looks like minor channel fading)
• BSR increase (looks like congestion)
• No indication of a software fault
What hook latency shows:
• Unmistakable spike — 7× the 1 ms slot budget
• Pure infrastructure signature — SINR unchanged
• No channel probe can see this

## Slide 13
In-Network Pre-Processing — Week 8 Extension
Computing statistics inside the eBPF program — no userspace required
Custom SINR codelet (C code):
• Hook: mac_sched_crc_indication — fires on every UL CRC PDU
Two algorithms inside the eBPF program:
• Variance: Welford online algorithm
• E[X²] − E[X]² — no stored history needed
• Sliding avg: 16-entry ring buffer
• Constant time update (no inner loop)
Why it matters:
• Anomaly detection logic runs at the gNB itself
• Sub-millisecond latency — no network hop to userspace
• Bandwidth saving: send avg/variance, not every raw sample
• New Grafana panels: SINR variance + sliding average

## Slide 14
Progress vs 12-Week Plan
All implementation phases complete — in Phase V (writing)
Phase I Wks 1–2 Foundation
Setup 5G sim + ZMQ link
DONE
Phase II Wks 3–5 Corelets
22 hooks 17 schemas
DONE
Phase III Wks 6–7 Evaluation
Dashboard Comparison
DONE
Phase IV Wks 8–9 Extension
Codelet math AI datasets
DONE
Phase V Wks 10–12 Conclusion
Validation Thesis writing
IN PROG
Deliverables
✓ Source code (codelets, scripts, pipeline)
✓ AI-ready datasets (CSV + HDF5, 5 621 samples)
✓ Setup guide and all documentation
✓ Anomaly collection report (35 scenarios)
✓ Janus vs Standard comparison (live data)
✓ Custom codelet documentation
○ Bachelor Thesis Report
○ Final presentation

## Slide 15
Summary of Contributions
1. Full 5G NR Telemetry Pipeline
22 jBPF hook points · 17 schemas · 1 ms granularity · 45-panel Grafana dashboard
2. ZMQ Channel Broker
GRC Python broker: AWGN + Rician/Rayleigh + EPA/EVA/ETU + interference + time-varying scenarios
3. Baremetal Installation
Fixed 10 eBPF verifier failures + 2 jrtc-ctl bugs + YAML config keys to get the full stack running
4. Two Labelled AI-Ready Datasets
5 621 samples · 19 features · 4 classes · 35 scenarios · scenario-based train/test split
5. Key Finding — Hook Latency as Fault Detector
Only metric that distinguishes scheduler faults from channel impairments · 7× spike · invisible to standard
6. Custom In-Network Codelet
SINR variance + sliding window computed inside eBPF at 1 ms — no userspace post-processing

## Slide 16
Remaining Work — Phase V
Thesis Writing (Week 11):
• Chapter: System architecture and implementation
• Chapter: Evaluation — jBPF vs standard comparison with live plots
• Chapter: Anomaly detection — dataset description, key findings
• Chapter: Conclusion and future work
Optional extensions (if time permits):
• Train a lightweight anomaly classifier on the collected dataset
• Evaluate CPU overhead at multiple traffic rates (10/25/50 Mbps)
• Extend custom codelet to output an anomaly score directly
Hardware (USRP) Bonus
Project plan explicitly designs for ZMQ simulation.
Hardware (USRP B210/X310) is optional bonus only.
If time permits after thesis draft:
• Replace ZMQ with real USRP radio
• Run codelets on live air interface
• Compare simulated vs real-world hook latency
Risk mitigation: do NOT attempt if it jeopardises the report deadline.

## Slide 17
Thank You
Questions?
github.com/MaximBitiu1/srsran-telemetry-pipeline
22
jBPF hook points
17
Telemetry schemas
45
Grafana panels
5 621
Labelled samples
3.3%
CPU overhead
7 000+
µs fault spike